## Slide 2: RRT )Renal Replacement Therapy(

## Slide 3: HD
IRRT
HD
HF
HDF
HDF on_line
CRRT
SCUF
CVVH
CVVHD
CVVHDF
SLEDD

## Slide 5: HD
Ultrafiltration
Fluid Transport
Diffusion
Convection
Adsorption
Solute Transport
Molecular Transport Mechanisms

## Slide 11
Composition of Fluid

## Slide 13: HDF
Definition
Is a form of renal replacement therapy that utilizes convective and diffusive clearance. Compared with hemodialysis, HDF allows increased clearance of larger-molecular-weight toxins and may be associated with improved clinical outcomes.
High-flux filter (sieving coefﬁcient >0.6 for β2-microglobulin)

## Slide 14
Notes: AGEs: Advanced glycation end products

## Slide 16
Replacement / Dialysate solution
HDF requires the infusion of significant amounts (at least 15 to 20 and up to 150 L) of fluid, called infusate, into the patient to replace the ultrafiltrate. This infusate fluid must be sterile and pyrogen free since it is infused directly into the blood. In addition, the rate of infusion must be accurately controlled so that fluid balance errors do not occur.
The infusate is either provided from the manufacturer in bags or generated by filtering the dialysis fluid within the dialysis machine.
All CRRT techniques other than slow continuous ultrafiltration (SCUF) require the use of sterile dialysate/replacement fluids.
The composition of these solution can be varied extensively to achieve specific metabolic goals.
Alimitation of using sterile solution for CRRT is that they are acetate or lactate based.
More recently, bicarbonate-based solutions, which are better tolerated than lactat- or acetate-based solutions, have become commercialy available.

## Slide 18: HDF ON-LINE
in online HDF, the infusate is drawn from the main dialysis fluid flow
obviates the need for additional fluid-balancing systems.
The dialyzer used in online HDF is the same as in high-flux dialysis. The dialysis machine must be capable of producing ultrapure dialysis fluid.
The ultrapure fluid is produced by ultrafiltration of the dialysis fluid after the concentrates have been added.
In some systems, the ultrafilters are reused between treatments and disinfected as part of the machine's normal disinfection process.

## Slide 19: MODS OF HDF
Post-dilution HDF
Pre-dilution HDF
Mid-dilution HDF
Mixed dilution HDF
push–pull HDF

## Slide 20
Post-dilution
HDF
In post-dilution HDF, the replacement ﬂuid is infused downstream of the dialyser, usually into the venous bubble trap.
Infusate rate: 20_25 % of blood flow rate
Blood flow rate : at least 350 mil/min
Increasing hemoconcentration
Raise TMP,causing alarms
Increasing risk of clotting
Needs for filter exchang

## Slide 22: Pre-dilution HDF
In predilution HDF, the infusion dilutes the blood components before ultrafiltration takes place.
Reduces risk of fouling- clotting
Lower clearance
Infusate rate : over 60% of blood flow rate

## Slide 28: Microbiological Safety
The generation of ultrapure infusate
Carefully monitoring and maintaining the dialysis equipment
Use of the correct disinfectant
Use multiple ultrafilters

## Slide 30: CRRT
SCUF
Siow Continuous Ultrafiltration
CVVHD
Continuous Veno-Venous Hemodialysis
CVVHDF
  Continuous Veno-Venous Hemodiafiltiation
CVVH
Continuous Veno-Venous Hemofiltration
Primary goal
Remove patient fluid
Primary goal
Achieve small,medium,and large molecule clearance
Remove patient fluid
Primary goal
Achieve small molecule clearance, remove patient fluid
Primary goal
  Achieve small,medium,and large molecule clearance
  Remove patient fluid
The choice of modality is dependent on several factors including:
Availability _cost_physician expertise_hemo-dynamic stability_the primary purpose of the procedure(fluid removal vs solute clearance)

## Slide 31: CRRT
Better solute clearance
Hemodinamic tolerance, slower ultrafiltration
Removal of inflammatory mediators
Reduction of core body temperature
Improvement of lactic acidosis
Improved nutrition
Removing myoglobolin in crush syndrome
Decreasing intracranial pressure in cases with cerebral edema
Higher cost
Increased need for anticoagulation
Unavailability in most center
Needs to trained staff
More delayed correction of uremic signs
Advantages
Disadvantages

## Slide 32
The Role of Solution in CRRT
Dialysate and Replacement fluids are used to facilitate the removal of solutes from the patients blood using the basic principles of molecular transport
Principle | SCUF | CVVH | CVVHD | CVVHDF
Dialysate | NO | NO | YES | YES
Replacement Fluid | NO | YES | NO | YES
What is removed | Fluid | Fluid & Solutes | Fluid & some Solutes | Fluid & Solutes

## Slide 33
CRRT dose (ml/kg/hr) = Effluent (dialysate fluid + replacement fluid + patient net UF)
EXAMPLE | 
Dialysate | = 1000 ml/hr
Replacement fluid | = 1000 ml/hr
Patient net UF | = 200 ml/hr
Patient weight | = 70 kg
Prescribed dose ml/kg/hr | = 31.4 ml/kg/hr
Best evidence to date supports dosing a minimum of 20_25 ml/kg/hr in all modalities ( CVVH , CVVHD, CVVHDF)
It is usually necessary to increase the prescription to ensure the prescribed dose is delivered.Frequent assessment of actual delivered dose is recommended.
In determining a prescription of RRT it is mandatory to consider parameters other than small-solute clearance, such as :
patients fluid balance
Acid-base and electrolyte homeostasis
nutrient

## Slide 34: CVVH
CVVH with pre-dilution
Pre-dilution prevents hemoconcentration within the filter
This prevents a surge in Hct, platelets & clotting factors within the filters and may help prolong filter life
However, pre-dilution decreases the efficiency of CRRT (less clearance) by diluting the solutes before they enter the filter
The solute dilution effect is dependent on plasma fiow into the filter which depends on pump blood fow and hematocrit.

## Slide 35: CVVH
CVVH with post-dilution
Post-dilution will lead to hemoconcentration within the filter
This will lead to a surge in Hb,platelets and clotting factors within the filters
This hemoconcentration may contribute to decreased filter life
The hemoconcentration effect will be less if the blood flow is greater
However, post-dilution will preserve the efficiency (more clearance) of CRRT by NOT diluting the solutes before they enter the filter

## Slide 36: CVVH
CVVH with combined pre and post-dilution
Combined pre and post dilution will lead to a lesser degree of hemoconcentration within the filter than post dilution
This will lead to an attenuated surge in Hb,platelets and clotting factors within the filters
This limited hemoconcentration may contribute to decreased filter life
However, per-dilution will decrease the efficiency of CRRT by diluting (to a lesser degree then pure pre-dilution) the solutes before they enter the filter

## Slide 37: CVVHD
Dose not require high blood flows
Plasma flow even at a blood flow of 100 ml/min will always exceed dialysate flow
Full equilibration occurs with clearance of small solutes similar to post-dilution CVVH but without hemoconcentration
Clearance is diffusive with little convevtion
Diffusive clearance (hemodialysis) differs from convective clearance (hemofiltration) in that it has little ability to remove middle molecules (cytokines,beta2 MG, vancomycin, teicoplanin)

## Slide 38: CVVHDF
Combines diffusion and convection
Circuit set up “more complex”
Clearance depends on the degree of pre-dilution
The changes in Htc will be attenuated compared to CVVH if the D to H RATIO = 50:50
Technique used in ATN and RENAL trials to allow similarities between standard and intensive CRRT without excessive hemoconcentration

## Slide 39: SLEDD
Advantage of SLEDD
Less cumbersome technique
Patient mobility
Decreased requirments for anticoagulated
Hemodinamic stability
Better correction of hypervolemia
Adequate solute removal
Cost lower than CRRT

## Slide 40
Prescription Comparison Summary
 | IHD | SLEDD | CRRT
Dose | KT/V or URR | ml/kg/hr or KT/V or URR | ml/kg/hr
Duration | 3_6 hr | 6_12 hr | 24 hr
Blood flow (Qb) | 150_450 ml/min | 100_200 ml/min | 150_200 ml/min
Fluid Used | Dialysiate only | Dialysate only | Dialysate & Replacement
Fluid Rate | 300_600 ml/min | 100_300 ml/min | 15_60 ml/min
Dialysate Composition | Non Sterile Dialysate | Non Sterile Dialysate | Sterile Dialysate & Replacement
Typical Net Fluid Removal Rate | Typical Net Fluid 0-1000 ml/min | Typical Net Fluid 0-500 ml/min | Typical Net Fluid 0-200 ml/min

## Slide 41
خدا قوت